## Slide 2
Semiconductor & Diode
UNIBIASED P-N JUNCTION
Empty holes
P-N Junction
there is a difference in the concentration of holes and electrons at the two sides of a junction, the holes from the p-side diffuse to the n-side and the electrons from the n-side diffuse to the p-side
What’s the direction of the intrinsic electric field?
However, in open circuit charged particles cannot move freely, resulting in the fo layers. And the electric field is from N-side to P-side.
UM-SJTU JOINT INSTITUTE
n- type
material
p- type
material
Free
electrons
Depletion
Region